## Slide 1: On Video
4c8
handout written by Prof. David Corrigan, based on Prof. Anil Kokaram material

## Slide 2: Video
A Background to Film, Video and Analogue & Digital TV/Video Formats
Exploiting Temporal Redundancy is key to digital video processing
  A process called motion estimation or optical flow
Video processing applications
  Focus on compression
  MPEG2/MPEG4

## Slide 3: Film
First Moving Pictures were on film
First moving images 1872 because of a bet on a horse
  Does a horse have all 4 hooves off the ground at any stage its trott?
Film is an analog medium but is discrete in time.
  it consists of a series of images known as frames

## Slide 4: Yes

## Slide 5: TV
TV is a technology for the transmission and reproduction of moving pictures
Rasterisation allowed images to be converted into 1D signals for transmission
  Signals are continuous horizontally but discrete vertically and in time
CRTs used to project the signal.
John Logie Baird first to show that it could be used to transmit moving images.

## Slide 6: TV
Nov 2nd 1936 BBC launched first regular “High Definition” TV Service
1953 3M viewers for coronation of queen = TV comes of age
Colour in 1954 in the USA (NTSC)
Europe used PAL and started colour in 1967

## Slide 7: Video Recording
A method for storing TV signals on magnetic tape.
Came along after TV was invented .. Bummer
1950 RCA = longitudinal tape 6m/sec (early tapes used to be made of steel and burst a lot)
1953 = Ampex corporation helical scan (yea!)
1972 Philips home video
1978 Betamax (Sony) Vs VHS (Panasonic)
1980 VHS standard
1995 Digital Betacam, Digital-S [Broadcast]
1998 DVD and Digital
2007 HD, DV, Blu-Ray, HDV

## Slide 8: Analogue Video
NTSC
PAL

## Slide 9: Progressive V Interlaced

## Slide 10: Interlacing makes it difficult to grab still frames from a TV
Odd Field
Even Field
2:1 Interlaced Frame

## Slide 11: NTSC v PAL
 | PAL | NTSC
Colour Space | YUV | YIQ
Number of Lines | 625 (576 visible) | 525 (480 visible)
Frame Rate | 25 | 30
Interlaced | Yes (50 Hz) | Yes (60 Hz)

## Slide 12: Digital Video Capture

## Slide 13: Digital Video Capture

## Slide 14: Getting Colour

## Slide 15: CCD v CMOS
Many consumer cameras use cheaper CMOS sensors
CMOS sensors use a “rolling shutter”
  the sensor is exposed line by line rather than at once
  this can lead to problems though

## Slide 16: Digital Video Sizes & Formats

## Slide 17: Digital Video Sampling

## Slide 18: Pictures in Motion
Motion is a key concept in video processing.
Motion Estimation or Object Tracking is a key stage in nearly all video processing tasks
  compression, video object segmentation, video denoise
We will look at a simple model for motion estimation for video sequences.
We will explore some well known techniques

## Slide 19: Pictures in Motion
Pinhole Camera Model
Pinhole/Lens
Imaging Sensor (eg. CCD)

## Slide 20: Projective Geometry
Pinhole

## Slide 21: Estimating Object Motion
Not usually possible to estimate 3D Object Motion single video sequences.
It is possible when you have more than 1 camera capturing the object
  V. interesting for multiview sequences (3D TV and 3D Cinema)
Will assume world is 2D and develop a simple model to describe the motion on a 2D plane

## Slide 22: 2D Motion

## Slide 23: Motion Model
We are assuming that a pixel at a position has the same value as a pixel at location in frame k.
is the motion of the pixel. In general each pixel can have a different motion so we represent it as a function

## Slide 24: Complications
Luminance/Colour changes.
Occlusion.
Ill-posed Problem.
Aperture Effect.
Local versus global.
Model Complexity – Should we not consider rotation and scaling?
Lens Distortion.
Grain/Noise.

## Slide 25: Displaced Frame Difference
If then we can define the Displaced frame difference as
To find the optimum motion field we need to find the motion vector field that minimises the DFD
  minimises the sum (or mean) squared (or absolute) DFD.
or

## Slide 26: Basic Strategies
Exhaustive Search/Block Matching
  Try every possibility until the minimum is found
  Easy to implement, suitable for hardware
  Brute force => computationally intensive.
  Limited precision and range
Gradient-Based Approaches (incl. Optical Flow)
  Gets a closed form solution for motion using Taylor Series
  Can give infinite precision
  Only accurate for small motions
  Harder to implement

## Slide 27: Block Matching (Full Motion Search)
Example of exhaustive search method
Image is divided into blocks and a motion vector is found for each block.
  Assumes that the motion is translational
  Gets around the ill-posedness
User/Engineer must decide:
  Block Size
  Range of Motion Vector Candidates
  Precision of Motion Vector Candidates

## Slide 29: Full Motion Search Block Matching
For Each Block
  For each candidate vector
    Calculate the block DFD
    Calculate the Sum/Mean Absolute Error of the DFD
    Choose the Vector v that minimises the mean absolute error

## Slide 30
N is the block size
w is the search radius

## Slide 31
Note: Motion Estimation is typically done on the luminance channel only

## Slide 32: Examples

## Slide 33: Examples

## Slide 35: Examples

## Slide 36: Measuring Performance
Quality
  Mean Absolute (or Squared) error between the current frame and the motion compensated previous frame.
Computation
  From execution time
  But need to count number of operations as well.

## Slide 37: Comparing Quality
DFD with Motion Compensation
DFD without Motion Compensation

## Slide 39: Comparing Quality
Motion Compensation
No Motion Compensation

## Slide 40: Computational Efficiency
To calculate the vector for one block
  There are candidates (assuming vectors accurate to 1 pixel)
  To calculate the mean absolute error you have to do 1 subtraction, 1 absolute value operation (or mult for mean squared error) and 1 addition per pixel.
  If the blocksize is then the total number of ops is per block
  There is an extra operation to find the min of values but the cost is much less compared to calculating the MAE.
Quadratic Order of Complexity wrt search radius
  If we double w, 4 times more ops are needed
  Not great

## Slide 41: Improving Complexity
Motion Detection
  Only do motion estimation where the frame difference is large

## Slide 42: Pixel Difference for Motion Detection
Frame n-1
Frame n

## Slide 43: Pixel Difference for Motion Detection
Frame n-1
Frame n

## Slide 44: Pixel Difference for Motion Detection
Smoothed abs(PD)
Threshold = 5
Threshold = 5
Low Pass Filtering of the DFD

## Slide 45: Motion Detection Algorithm for Block Matching
Find the mean absolute error for each block.
Apply the following threshold to the MAE or each block

## Slide 47: Improving Complexity
2. Don’t test all of the candidates.
Eg. The 3 step search
1. Search subset of evenly spaced candidates and find best candidate.
2. Use result of step 1 as centre for another search on a more closely spaced grid.
3. Repeat step two on a finely spaced grid.

## Slide 48: 3-Step Search
Each intersection of lines corresponds to a potential motion candidate – the 3 step search allows you select the a vector without testing each candidate.
In step 1 the number of candidates for which the error is evaluated at is
In steps 2 and 3, the error is evaluated for 8 further candidates. (The centre candidate will have been evaluated in the previous step)
However the result is sub-optimal and therefore there will be a slight increase in the overall MAE.
So if w = 16 then candidates are evaluated for the full motion search and only
are evaluated in the 3 step search

## Slide 49: Improving Complexity
3. Do a search at multiple resolutions and scales
The basic idea is to do the bulk of the search on lower resolution versions of the images.
For example if we have a block size of 16 and a search radius of 12 then at half picture resolution the equivalent block size would be 8 and search radius would be 6.
We can then do a smaller search at full resolution

## Slide 50: Multiresolution Block Matching
Building the low pass pyramid.
For both frames we loss-pass filter and then downsample by a factor of 2. This is repeated multiple times
The low-pass filter prevents aliasing. A gaussian shaped filter mask is typical.
Level 0
Level 2
Level 1
2D Gaussian mask – 15*15 taps

## Slide 51: Multiresolution Block Matching
Level, l | Block Size | Search Radius
0 | N | 
1 |  | 
2 |  | 
l |  | 
Level, l | Block Size | Search Radius
0 | N | 
1 |  | 
2 |  | 
l |  | 
Algorithm:
Generate the L level pyramid for the current and previous frames. Level l = 0 is the full resolution and l = L-1 is the smallest resolution.
Set the initial level to l = L-1 and initialise all vectors to 0.
Generate an estimate of the motion field at level l, centring the search on the initial vector for that block.
If l=0 then go to step 7.
Propagate the motion field to level l -1. It is the initial field for level l -1.
Set level to l = l -1 and Go to Step 3.
Stop.
Block and Step Sizes to be used for the motion search at each at each level

## Slide 52: Multiresolution Block Matching
The number of ops at level l is
So consider the example where we want to estimate motion where
the block size, N = 16
The search radius, w = 20
The Number of levels, L = 3
Level, l | Number of OPs
2 | 
1 | 
0 | 
Total | 
Level, l | Number of OPs
2 | 
1 | 
0 | 
Total | 
The number of ops for a full motion search is
= 1291008 ops
So a big drop in the number of computations.

## Slide 53: Gradient-Based Motion Estimation
We can solve for the minimum square error
exactly if we express using a Taylor Series,

## Slide 54: Gradient-Based Motion Estimation
If we ignore the higher order terms we get
And if we substitute this expression we get
With this approximation it now appears we can solve for using calculus (ie. Get derivative of RHS and set to 0)
However, it is still necessary to make spatial smoothness assumptions to get a solution.

## Slide 55: Gradient-Based Motion Estimation
There are two main ways which in which spatial smoothness contraints are added
Assume all pixels in a block share have the same motion vector.
  Lucas & Kanade, Biemond et al., Kokaram etc.
Consider , hence
We can write down 1 equation for each pixel, there are 2 unkowns per pixel (ie. Horizontal and vertical motion) and is underdetermined. However, …

## Slide 56: If all pixels in an N*N block have the same motion…
For each block e then get N2 equations
with only 2 unknowns
This can be written in matrix
form as

## Slide 57: Solving for d
Because there are more equations than unknowns only a least squares estimate is possible
So it is possible to estimate d without having to try every possible motion vector.
It can give estimates to “infinite” precision.
However, the higher order terms in the Taylor Series can only be ignored for small values of d. Therefore the result is only accurate if the motion is small.
is not a square matrix
is a square matrix

## Slide 58: Iterative Solution
The limited range can be overcome somewhat using multiresolution and an iterative approach.
  Say we have an approximate solution di . Then we take the Taylor Series about x + di instead of x.
  This results in a linear system of equations. Once we estimate ui and hence d, we set di = d and repeat the process. Eventually the estimate will converge (ie ui ≈ 0).
  This is an example of the Gauss-Newton optimisation algorithm.
Update to current guess
True motion
current guess

## Slide 59: 2. An Alternative Approach
The well known Horn & Schunck algorithm does not assume the same motion over a block. Instead it assumes that the motion varies smoothly at each pixel.
We add this to the Taylor Series constraint
and therefore we try to find the motion that minimises
This looks tricky but it too reduces to solving a system of linear equations
Motion is smooth if Ds(x) is small

## Slide 60: The Aperture Effect
The aperture effect causes ambiguity in motion estimation when the block size is too small.
The problem is that multiple candidate vectors will have the same error.
It is a problem of data quality and is a problem for all types of motion estimator.
Can be mitigated by increasing the block size or through multiresolution.

## Slide 61: Aperture Effect
Aperture Effect is associated with
  Regions of Uniform intensity
  Straight Edges
Corners are immune to it and are good features for motion estimation
  Feature detectors such as Harris, SIFT, Shi-Tomasi etc detect corners
  Used for tracking and matching applications in computer vision.

## Slide 62: Example of the Aperture Effect
Current Frame with Vectors
Past Frame
Only accurate vectors are at the corners.
Vectors inside the edge are incorrectly estimated as 0.
At the edges only the component of motion perpendicular to the edge is correct.

## Slide 63: Pathological Motion
Types of behaviour that typically cause motion estimation failure
  Fast Motion – eg. the size of the motion bigger than the search window for
  Occlusions – The data might not be present in both views.
  Transparency/Reflections – in effect their could be two motions, eg. one for the reflection and one for the mirror.
  Non-rigid objects – (eg. Hair, flames etc) Motion is not rigid at these points
  Motion Blur.

## Slide 64: Summary
We have detailed a model to estimate motion in images.
We have looked at block matching in detail & also looked at gradient-based approaches.
We have explored the use of multiresolution and other approaches for optimising block matching.
We have looked at the aperture effect and potential issues affecting robustness.